## Slide 1: Side channel attacks
Computer Security - Ymir Vigfusson

## Slide 2: Background
An algorithm or software can be designed to be provably secure.
  E.g. cryptosystems, small OS kernels, TPM modules, ...
  Involves proving that certain situations cannot arise
  Or that breaking them would be just as hard as doing something incredibly tedious
    Such as factoring large numbers
But what about the environment in which these algorithms or software are located?

## Slide 3: Side channel attacks
Correlation between physical measurements during computation (side channel) and the internal state of the computer
Attacks that exploit the physical implementation of a system

## Slide 4: Side channel attacks
Timing attacks
  Measure time between computations
Power monitoring attacks
  Measure varying power consumption during computation
Electromagnetic attacks
  Measure radiation from devices (e.g. monitors)
Acoustic attacks
  Listen to sounds emitted during computation
Differential fault analysis
  Deliberately provoke faults in computation to discover secrets
Data remanence
  Resurrect data that was thought to have been deleted
    Such as the memset() of the password example from first class

## Slide 5: Early attacks
1956: Operation ENGULF
  British&US did not want to fund Egyptian President Nasser to build the Ashwan High Dam so he turned to the Soviets
  Nasser takes over the Suez Canal, formerly under British&French control, to collect tolls on ships
  MI5 places bugs in the Egyptian embassy to listen to 2-3 rotors of Hagelin cipher machines that were communicating sensitive information with French and Soviets
    Soviets helped sweep the embassy for bugs, but left the MI5 one!
Relies on an attack of the physical implementation of the Hagelin cipher machine: a side channel attack
  What was the side channel?

## Slide 6: Early attacks
1946-1952: The Thing
  Soviets gave US ambassador to the USSR 2“ hand crafted seal for his office.
  Ingenious passive listening device inside based on a spring by Theremin
  Spies shot radiowaves at 330MHz at distance to activate microphone and listen in for 6 years
  Discovered by a stroke of
  luck by a technician

## Slide 7: Early attacks
1947-ish: Laser microphone („Buran“)
  Theremin also developed a technique for showning a low power infrared beam on glass windows to detect vibrations from sound at distance
  Used by precursor of KGB to spy on U.S., U.K. and French embassies in Moscow
  Works best with smooth
  surfaces, hence the use of
  rippled glass by security
  agencies...

## Slide 8: Early attacks
1980: Soviets accused of planting bugs in IBM Selectric printers to listen to the sound of the type ball as it rotates and strikes the paper
  Allows the spies to “listen“ to what was being printed

## Slide 9: Early attacks
1985: Wim van Eck eavesdrops CRT/LCD emissions
  Oscillating electronic currents inside video displays generate electromagnetic radiation in the radio frequency range that correlated with the image being shown on the screen.
  CRT: Cost ~$15.
  LCD (2004): Cost ~$2000

## Slide 10: Early countermeasures
TEMPEST: NSA specification for protection against side-channel attacks. Been partially declassified.
  U.S. initially playing catch-up to Soviet intelligence on exploiting emanations
  Sets up zones depending on how physically close an attacker can get (0-100m)
  Add extra noise (shielding) when required:

## Slide 11: More modern attacks
1991: Briol shows that sounds from dot-matrix printers leak significant details on the contents being printed
2002: Loughry and Umphress show that the LED lights on networking equipment are heavily correlated with the data they are transmitting
  Could effectively listen in on all network traffic
  Mostly theoretical
Loughry & Umphress (2002): Information Leakage from Optical Emanations

## Slide 12: More modern attacks
2004: Asonov and Agrawal of IBM show that keyboard and keypads (such as on ATMs) emit different sounds for different keys
  Practical experiments by Berkeley in 2005 for covert listening for passwords, PINs, etc.
  Needs a training phase (each key 100 times)
2005: Zhuang, Zhou and Tygar recover 96% of English text from keyboard sound recording
  No training required, if recording is at least 10 min.
Zhuang et al: http://www.tygar.net/papers/Keyboard_Acoustic_Emanations_Revisited/ccs.pdf

## Slide 13: Timing attacks
2004: Shamir and Tromer use timing attacks against CPUs
  Different operations cause variable ultrasonic noise from the capacitors/inductors
2013: Shamir, Tromer and Genkin use techniques to listen to GnuPG via a cell phone
  Able to extract 4096-bit private key by listening to the computation

## Slide 14: More recent attacks
2007: Bortz, Boneh and Nandy show observing timing data of TCP packets (even HTTPS) allows you to infer:
  number of Facebook friends (effectively),
  contents of shopping cart,
  and so forth
Recent discussions about impact on TOR: check whether a connection exists between a user and a server
  Think oppressed journalist and Twitter via TOR
  Spoof TCP packets to halve the window size of a connection
http://www2007.org/papers/paper555.pdf

## Slide 15: More modern attacks
2011: Thermal imaging
  Mowery et al. show how ATM keypads can be broken by looking at residual heat from keypressed by a target user
  Works up to a minute after the user enters the password
  Reduces search space from 10,000 to about 24 for 4-digit PIN
https://www.usenix.org/legacy/events/woot11/tech/final_files/Mowery.pdf

## Slide 16: More modern attacks
2011: Traynor et al. from Gatech show how the accelerometer on a cell phone can decode vibrations emitted from a nearby keyboard
  Effectively a listening device for any app on the phone
  Sampling rate much smaller than with previous gizmos
    Perhaps 100Hz on iPhone 4, or 400x less then Asonov et al.
  Instead, modeled keypress events
    Models proximity between keys, left/right, duration of keystroke, ...
  This timing attack was investigated in depth for SSH passwords in 2002

## Slide 17: More modern attacks
2009: Vuagnoux and Pasini capture electromagnetic emanations directly from keyboards at 20m distance
  No need for other wires providing physical support for emanations
Demo:
  http://vimeo.com/2008343
http://lasec.epfl.ch/keyboard/

## Slide 18: What‘s happening today
2014: Timing attack to identify Google users
  Want to know if a particular Gmail address being used?
  Link to a picture that only the authenticated user could access
  Triggers onerror() in Javascript in 891ms if image was accessible, but 573ms if not.
http://thehackernews.com/2014/09/unmasking-google-users-with-new-timing.html

## Slide 19: What‘s happening today
http://thehackernews.com/2014/09/unmasking-google-users-with-new-timing.html

## Slide 20: SAP flaw

## Slide 21: SAP flaw
Roughly equal to the following C code:
What‘s the flaw? How would you exploit it?
int passwordCheck(char *truepw, char *pw) {
while (*truepw) {
if (*truepw != *pw) {
printf ("Password check failed\n");
return -1;
}
}
return 0;
}

## Slide 22: SAP flaw
2014: SAP Router Password Timing Attack
  Router disallows connections based on a table, unless the correct password is specified.
  Just walk linearly through the passwords, asking:
    „Hey, is the next character A? No? How about B? ...“
  Illustrates a general problem for cryptosystems (and caches)

## Slide 23: Today!
2016: Cache side-channel attacks
  Has something been requested before?
2017: Timing attack on SGX Enclave
  Work done at Georgia Tech (Taesoo Kim et al.)
2017: Optical side-channels
  See the photons that are emitted as part of your computation!

## Slide 24: Countermeasures
Side-channel attacks rely on merging information from the side channel to the original data
  Approach 1: Eliminate side channels
    Put government buildings in a Faraday cage (anti-TEMPEST)
    Jam the channels / add random delays
    Let execution paths not depend on secret information (PC-secure)
    Myers et al. (2011) Predictively mitigate timing attacks
  Approach 2: Remove correlation between side channel and original data
    Blinding in cryptography
      In RSA, multiply encrypted ciphertext with a random number before decrypting, then factoring it back out.
http://www.cs.cornell.edu/andru/papers/ccs11.pdf