Air Resistance Force

Abstract: This experiment measured the force of air resistance in a system involving objects with varying mass and varying surface area by tracking the free fall motion of the object after being dropped from approximately two meters to the ground. The force of air resistance can easily be calculated using the following: starting with F = ma, we then calculate the total sum of forces present, ∑F = F_g - F_air, then F_g - F_air = ma, which gives us F_air = m(g - a). Two experiments were conducted wherein multiple trials were conducted. The first experiment involved calculating acceleration of similar object, sponged, and repeating the same experiment while cutting the surface area in half twice for a total of three sets of data. The second involved using different objects, weighted sponged, boxes, and textbooks, and conducting the same experiment using these objects with varying mass and surface area. We found a linear trend between surface area of objects and the force of air resistance on the objects. When recording the motion of the falling objects, the camera was placed on it’s side to reduce as much as possible the systemic error that arises from the rolling shutter of the camera. Insights into how the orientation of the camera affects accuracy in tracking objects as well as performing the experiment with enough variance in surface areas will be used to guide future experiments, in an attempt to reduce systemic error as much as possible.

Report written by: Wesley Harmon

Lab Partner: Justin Bier

November 30, 2016

INTRODUCTION: Initially it may seem as though both surface area and mass would play an important role in calculating the force of air resistance on a falling object, but as we have shown in our experiment, the results simply point out a relationship between surface area and force of air resistance. Our goal of this experiment was to show this relationship between surface area and force of air resistance. By our formula F_air = m(g-a), you can see that calculating the force of air resistance does not involve the use of surface area for any given calculation. The force of air resistance is defined as the resistive force that an object experiences while free-falling in an atmosphere consisting of a relatively constant atmospheric pressure at a given altitude. That is, since all objects we experimented on were dropped from approximately the same altitude, thus removing the variable of having varying atmospheric pressure. Mathematically modeling the force of air resistance on a freely falling object is quite a complex problem, but upon analyzing the free body diagram of said object, it is clear that there is at least one relatively simple way to calculate this force using the formula above.

PROCEDURE: For setup, two meter sticks were used to allow us to drop all objects from approximately the same height of two meters. The objects involved in the final experiment were a an empty printer paper box (dropped the bottom facing the ground to avoid extra drag from the open face of the box), a textbook, a notebook, an empty video camera box, two sponges taped beside each other, two sponges stacked on top of each other, a single sponge, and the single sponge with a 20g weight added. Firstly, however, the surface area and mass of all objects were measured and recorded. For each object, the given object was dropped and its motion from release to the ground was recorded using a video camera placed on its side. Each object was dropped multiple times, roughly 7 trials for each object. Motion Tracking Software (Tracker) then allowed one to the track the path of the falling object as it fell to the ground. Approximately 12 frames were used to track the objects’ motions. Tracker was then formatted to output the velocity of the object with respect to time for the utilized frames and the data was imported into Excel for further analysis for each trial on each object. The average acceleration was then calculated by using a velocity vs time plot for each trial, generated in Excel. Then, for each object, the force of air resistance was calculated using the above formula: F_air = m(g-a). The underlying uncertainty for each resistive force on each object as well as the average acceleration could then be calculated using the slope error formula and the standard error for acceleration. The uncertainty for each resistive air force was calculated to a 95% confidence interval.

RESULTS AND ANALYSIS: The tables on the next page represent the raw data obtained from two separate experiments, where the first column for each trial is Time (t) and the second column is velocity (v_{x}). The data shows the velocity of the object with respect to the given time for each trial conducted. The smaller table and plot on the following page represents the final data, the surface area of each object and it’s corresponding resistive air force. For the first week’s experiment, we encountered an issue when repeating the same experiment and cutting the surface area in half each time; the average acceleration of the smallest surface area was not theoretically possible, so the data was not used. To fix this, the second week’s experiment involved a similar overall strategy but different objects of varying mass and surface area were used instead of simply modifying the same object to produce a different surface area, thus the procedure explains all of the objects that were used only in the second set of experiments. However, data from the two sponges taped together, and then stacked on top of each other, were used because the data was sound. After the second set of experiments we were finally presented with data that was sound compared to our expectation, namely, that the acceleration of any given object could not exceed 9.8 m/s^2.

Table 1: Two sponges taped together side by side with a surface area of 0.026904 m^2
Mass: 0.0767 kg

Average acceleration = -8.6 +- 0.3

Table 2: A single sponge (weighted with 20g) with surface area of 0.00931 m^2
Mass: 0.045 kg

Average acceleration = -9.3 +- 0.1

From this data, one can see that the average acceleration for each object averaged to a value that is within what we would expect. But why would the final experiment from week one, where the surface area was 0.00697 m^2, give us an average acceleration of 11.231 m/s^2? There could have been systemic error in tracking the object, as the camera’s shutter produced a discrepancy between actual position and recorded position, but how is this reconciled with the sound data we obtained from other trials?

The final plot shows a very clear relationship between the surface area of an object and the force of air resistance. We can see clearly in the plot above that there is a linear trend between the two values. That is, as surface area increases, so too will the force of air resistance. This can be supported by a simply thought experiment. If you take a piece of paper and drop it along side a balled up piece of paper, you will immediately notice that the balled up paper drops to the ground quicker than the former. That is, the balled up paper will experience less resistive air force because there is less surface area for the air push against as the paper falls to the ground. So, with this simple experiment, it can be shown that, at least when it comes to objects of similar mass, the force of air resistance increases as surface area increases. Our data confirms that this is the case; our goal was to show that there is some relationship between surface area and force of air resistance, that seems to be independent of mass. However, how can this be the case, when calculating F_air involved directly using mass to obtain the value? Well, from the two tables provided on the previous page, it shows that as surface area increases, the acceleration of the object will decrease, and this seems to be independent of the masses.
Table 4: Surface Area of all objects in final report and their corresponding resistive air force

Surface Area vs. Resistive Air Force
sub-title
Surface Area (m^2)
Force of Air Resistance (N)
The uncertainty of the force of air resistance was calculated to a 95% confidence interval, including the fact that the error will propagate from determining the average acceleration for each object over all the trials. To calculate the error in acceleration, take for example the single weighted sponge. There were ten trials in total and since we are effectively estimating one value, velocity, the degrees of freedom will be 9. Then, given the average acceleration of -9.32412, and we want a 95% confidence interval, calculate the standard error by taking the standard deviation which came out to be 0.20675 of the accelerations and dividing by the square root of the number of trials: stderror = 0.20675/sqrt(10) = 0.06538. Then for a 95% confidence interval and degrees of freedom being 9, the uncertainty interval for this acceleration will be 0.06535*1.833 = 0.12, where 1.833 is the t-value for df = 9, at a 95% confidence interval. So, the uncertainty for the acceleration of the weighted sponge is 9.3 +- 0.1. This same process was used to calculate the uncertainty for all average accelerations. Then, to calculate the uncertainty for the force of air resistance vs. surface area plot we are now using the slope error formula: error = slope*sqrt((1/(R^2) – 1) / N-2 ). So, the slope is 3.65 and N = 8, and our R^2 = 0.977, then the error in the slope is 3.65*((1/0.98 – 1)/ 6) = 0.229. Calculated to 95% confidence interval, the uncertainty in our slope is 3.65 +- (0.229*1.96) = 3.7 +- 0.5. The error for a given resistive air force was calculated as follows: for the weighted sponge, a = 9.3 +- 0.1, with degrees of freedom being N-2 since the calculation of each F_air involved the use of two estimated values. So, the standard deviation for F_air is 0.07781, calculated in Excel, and the standard error is 0.02751, calculated in excel using our obtained values. Calculated to a 95% confidence interval, 0.02751*1.943 = 0.054 , the error for the forces of air resistance.