Charge To Mass Ratio Of The Electron

ABSTRACT: The electron charge to mass ratio was an experiment that was used to calculate the ratio of the electron’s charge to its mass. A beam of electrons caught in a magnetic field shift their direction to produce a vibrant ring of a blue hue. Using relevant equations, once either the mass or charge of an electron was found in the first iteration of this experiment, the other would be known. The Helmholtz coils produce a uniform magnetic field at right angles to the electron beam, which is deflected in a circular path.

Report written by: Wesley Harmon
Lab Partner: Laura Briggs

February 20, 2017
INTRODUCTION

The e/m apparatus provides a simple method for measuring e/m, the charge to mass ratio of the electron. A beam of electrons is accelerated through a known potential, so the velocity of the electrons can be found from eV = 0.5mv^2 where V is the accelerating potential. The charge to mass ration of the electron is given by e/m = 125Va^2/32(Nμ_0*Ir)^2 where V is the accelerating potential, r is the radius of the electron beam path, a is the radius of the Helmholtz coils, N is the number of turns of each coil (N=130), I is the current in the Helmholtz coils, and the constant μ_0 = 4π*10^-7 T*m/A. The above equation was derived from the qvB = F_B where q here would simply be e, v is the velocity of the electrons, B is the magnetic field, and F_B is the force produced on the electrons by the magnetic field. We then get ma = evB which yield 0.5mv^2/r = evB, which finally gives us e/m = v/Br. From here we can derive e/m given above.

PROCEDURE

The power supplies were initially turned off. The Fluke meter was used as an ammeter and was configured to measure 0-2 amperes dc. The voltmeter was configured to measure 0-300 volts dc. The AC Voltage Adjust knob on the the SF-9584 Low Voltage AC/DC Power Supply was set to 6 volts. The toggle switch of the e/m apparatus was set to MEASURE. The DC CURRENT ADJUST knob of the SF-9584 was turned fully counterclockwise. The same was done to the DC VOLTAGE ADJUST. The 500 VOLT ADJUST knob on the SF-9584 was turned fully counterclockwise.

The DC VOLTAGE ADJUST knob was then turned until the output was between 6 V and 9 V. The DC CURRENT ADJUST and the HELMHOLTZ COIL – CURRENT ADJ knob were turned slowly, making sure that the current did not exceed 2 A. The accelerating potential was increased to between 150 and 300 volts using the 500 VOLT ADJUST knob on the SF-9584 power supply.

Once the cathode heated up, and the electron beam was produced, the FOCUS knob was adjusted to sharpen the beam. The accelerating potential, the current in the Heimheltz coils and the radius of the beam were measured and recorded, using proper techniques to avoid parallax errors. Two more trials were conducted using different accelerating voltages and/or coil currents.

Then, the current was turned off and a bar magnet was used to observe the effects of an external magnetic field, where the beam was shooting directly into the bulb of the apparatus. A vector diagram was drawn based on our observations.

RESULTS AND ANALYSIS

The table on the following page represents the raw data obtained from our experiment where six total trials were conducted. The first three trials held the accelerating potential at a constant of 217.3 V. The last three trials were conducted with a constant current in the Helmholtz coils of 1.53 A. The average e/m is given along with the standard error, given to a 97.5% confidence interval.

Our final electron mass charge ration was 1.57 +- 0.08 * 10^11 C/kg. The charge to mass ration of the electron is given by e/m = 125Va^2/32(Nμ_0*Ir)^2 where V is the accelerating potential, r is the radius of the electron beam path, a is the radius of the Helmholtz coils, N is the number of turns of each coil (N=130), I is the current in the Helmholtz coils, and the constant μ_0 = 4π*10^-7 T*m/A. The above equation was derived from the qvB = F_B where q here would simply be e, v is the velocity of the electrons, B is the magnetic field, and F_B is the force produced on the electrons by the magnetic field.

We then get ma = evB which yield 0.5mv^2/r = evB, which finally gives us e/m = v/Br. Using B = μ_0Ia^2N/(x^2+a^2)^3/2, and substituting this into e/m = v/Br, we can obtain the final equation for electron charge mass ration, by using the relationship between x and a. Because the electron beam was produced in the middle of the apparatus, that is, using x = 1/2a, we can finally simplify the equation to obtain e/m = 125Va^2/32(Nμ_0*Ir)^2. Then, using the values obtained from each of our separate trials, e/m could be found for each of our six trials.

The degrees of freedom was five, since the only estimated value was the radius of the electron beam, which could have introduced error into our results, due to parallax errors. To combat this, we had two of our team members measure the radius and the two values were averaged. Using degrees of freedom being 5, our t-critical value is 2.57 because we wanted a 97.5% confidence interval. So, using the standard error, stderr = 3065393706, and t value = 2.57, we get 3065393706*2.57 = 7.88E9. So, finally we can present our e/m ratio given to a 97.5% confidence interval, as e/m = 1.57 +- 0.08 * 10^11 C/kg, which is consistent with what we would expect. We expected the e/m value to have a magnitude of 10^11.